## Slide 1: Electrochemical Water Splitting
Hydrogen Production via Electrolysis

## Slide 2: What is Water Splitting?
Water splitting is the chemical reaction to split water into oxygen and hydrogen:
  2H₂O → 2H₂ + O₂
  Requires energy input (electricity in electrolysis)
  Hydrogen can be used as clean fuel

## Slide 3: Electrolysis Basics
Key Components:
  Anode: Oxygen Evolution Reaction (OER)
  Cathode: Hydrogen Evolution Reaction (HER)
  Electrolyte: Ion transport medium
  Catalyst: Reduces overpotential

## Slide 4: Types of Electrolyzers
Alkaline Electrolyzers
  Use KOH or NaOH electrolyte
  Mature technology, cost-effective
PEM (Proton Exchange Membrane)
  Use solid polymer electrolyte
  Higher efficiency, compact design
Solid Oxide Electrolyzers (SOEC)
  High temperature operation (700-900°C)
  Highest efficiency potential

## Slide 5: Catalyst Materials
HER Catalysts:
  Platinum (Pt) - best performance but expensive
  Nickel, molybdenum sulfides - alternatives
OER Catalysts:
  IrO₂, RuO₂ - noble metal oxides
  NiFe oxides/hydroxides - earth-abundant

## Slide 6: Efficiency and Challenges
Thermodynamic voltage: 1.23 V
  Practical voltage: 1.8-2.0 V (due to overpotentials)
  Energy efficiency: 60-80%
Challenges:
  Reducing catalyst cost
  Improving durability
  Scaling up production

## Slide 7: Applications
Green hydrogen production for:
  Energy storage (power-to-gas)
  Transportation fuel cells
  Industrial processes (ammonia, steel)
  Grid balancing with renewable energy

## Slide 8: Future Outlook
Growing demand for clean hydrogen
  Cost reduction through scale and R&D
  Integration with renewable electricity
  Target: <$2/kg hydrogen by 2030
  Key role in decarbonization